# Technical Bulletin

To: Per Distribution List							From: Doug Reiland

Date: 04/02/09

Subject: DY2008 Pattern Controller

Display Replacement

Bulletin 040209-05

The DY2008 Display Board (27.00001.103) was recently updated and may require slight modification to the mating connection plug on the Front Panel Microprocessor Board (28.00005.103). The new display will have an orange-colored connector that is not compatible with the Microprocessor Board’s receptacle housing. The receptacle housing must be removed from the Microprocessor Board to allow connection of the display plug. Use a small, flat bladed screwdriver to pry the press-fit housing up and off of the connection pins of the board. The orange plug from the display can be connected to the pins that remain once the housing is removed. Orient the orange connector so its clip is away from the board edge.

Below are illustrations of the above procedure.

1  2

3  4  5