# Technical Bulletin

To: Per Distribution List							From: Stewart Haddock, Brian Midgetté

Date: 07/17/08

Subject: Dynamelt M Series Version 5

Dynacontrol Hopper Empty

Bulletin 071708-02

ITW Dynatec has identified isolated instances of “Hopper Empty” appearing on the display on the Dynamelt M Version 5 software units that are not equipped with Low Level Detection. The system would display a hopper empty screen and initiate a 10 minute timer that causes the motors to stop once the time has elapsed.

To correct this occurrence a jumper wire should be installed at X4 to terminal #3 and #9 on the #1 CPU board. Split Hopper Units would require both main CPU boards to have the jumper.